Chip-8 User Manual
CreateAssembly.app (2021)

# Instruction Set Architecture
## 00E0 - CLS
Clears the display.
## 00EE - RET
Returns from the current subroutine.
PC = STACK[SP];
SP = SP – 1;
## 0nnn – SYS addr
Unused.
## 1nnn – JP addr
Jump to specified address.
PC = addr;

## 2nnn – CALL addr
Increment the stack pointer, store the program counter in the stack, then jump to given address.
SP = SP + 1;
STACK[SP] = PC;
PC = addr;
## 3xkk – SE Vx, byte
Skip the next instruction if the value stored in Vx is equal to the given number.
If (Vx == byte)
Then {PC = PC + 2};
## 4xkk – SNE Vx, byte
Skip the next instruction if the value stored in Vx is not equal to the given number.
If (Vx != byte)
Then {PC = PC + 2};
## 5xy0 – SE Vx, Vy
Skip the next instruction if the value stored in Vx is equal to the value stored in Vy.
If (Vx == Vy)
Then {PC = PC + 2};
## 6xkk – LD Vx, byte
Store the given value in register Vx.Vx = byte;
## 7xkk – ADD Vx, byte
Add the given value into register Vx.
Vx = Vx + byte;
## 8xy0 – LD Vx, Vy
Store the value of Vy in Vx.
Vx = Vy;
## 8xy1 – OR Vx, Vy
Bitwise-OR Vy into Vx.
Vx = Vx | Vy;
## 8xy2 – AND Vx, Vy
Bitwise-AND Vy into Vx.
Vx = Vx & Vy;
## 8xy3 – XOR Vx, Vy
Bitwise-XOR Vy into Vx.
Vx = Vx ^ Vy;
## 8xy4 – ADD Vx, Vy
Add Vy into Vx. Set VF to 1 if there is an overflow, or 0 otherwise.
VF = (Vx + Vy) > 255;
Vx = Vx + Vy;
## 8xy5 – SUB Vx, Vy
Subtract Vy from Vx and store the result in Vx. Set VF to 0 if there is a borrow, or 1 otherwise.
VF = Vx > Vy;
Vx = Vx - Vy;
## 8xy6 – SHR Vx [, Vy]
Shift Vx right by 1. Vy is deprecated and unused.
Vx = Vx >> 1;
## 8xy7 – SUBN Vx, Vy
Subtract Vx from Vy and store the result in Vx. Set VF to 0 if there is a borrow, or 1 otherwise.
VF = Vy > Vx;
Vx = Vy – Vx;
## 8xyE – SHL Vx [, Vy]
Shift Vx left by 1. Vy is deprecated and unused.
Vx = Vx << 1;
## 9xy0 – SNE Vx, Vy
Skip the next instruction if Vx does not equal Vy.
If (Vx != Vy)
Then {PC = PC + 2};
## Annn – LD I, addr
Set register I to the given address.
I = addr;
## Bnnn – JP V0, addr
Jump to the value in V0 + the given address.
PC = V0 + addr;
## Cxkk – RND Vx, byte
Store a random value, bitwise-AND’d with the given byte, in Vx
Vx = rand(0, 0xFF) & byte;
## Dxyn – DRW Vx, Vy, nibble
Load n-bytes starting at MEM[I]. XOR them onto the display (each byte occupies its own row) starting at (Vx, Vy). Will wrap horizontally and vertically if necessary. Set VF to 1 if there is a collision, or 0 otherwise.
Load n-byte sprite at MEM[I];
 XOR sprite onto the display at (Vx, Vy);
VF = collision;
## Ex9E – SKP Vx
Skip the next instruction if the value stored in Vx corresponds to a key that is currently pressed.
If (KEY[Vx] down)
Then {PC = PC + 2};
## ExA1 – SKNP Vx
Skip the next instruction if the value stored in Vx corresponds to a key that is not currently pressed.
If (KEY[Vx] up)
Then {PC = PC + 2};
## Fx07 – LD Vx, DT
Load the value of the delay timer into Vx.
Vx = DT;
## Fx0A – LD Vx, K
Block until a key is pressed. Store which key was pressed in Vx.
Block until key down;
Vx = key;
## Fx15 – LD DT, Vx
Load the value of Vx into DT.
DT = Vx;
## Fx18 – LD ST, Vx
Load the value of Vx into ST.
ST = Vx;
## Fx1E – ADD I, Vx
Add the value of Vx into I.
I = I + Vx;
## Fx29 – LD F, Vx
Store the location of the Vx’th sprite in I. The exact location may vary from emulator to emulator. However, most sprite data starts at MEM[0] and each sprite has a length of 5 bytes.
I = &SPRITE[Vx];
## Fx33 – LD B, Vx
Store the BCD representation of the given register in memory, starting at address I.
MEM[I] = floor(Vx / 100);
MEM[I+1] = floor(Vx % 100 / 10);
MEM[I+2] = Vx % 10;
## Fx55 – LD [I], Vx
Store contents of registers V0 through Vx in memory, starting at address I.
MEM[I+0] = V0;
MEM[I+1] = V1;
MEM[I+2] = V2;
…
MEM[I+x] = Vx;
## Fx55 – LD [I], Vx
Load x bytes of data from memory, starting at address I, and store them in registers V0 through Vx
V0 = MEM[I+0];
V1 = MEM[I+1];
V2 = MEM[I+2];
…
Vx = MEM[I+x];

# Assembler
# Numbers
### Representation
; All of the following instructions load 19 into their respective registers / LD V0, 19 ; Decimal / LD V1, 0x13 ; Hexadecimal / LD V3, 0b10011 ; Binary / LD V5, 0o23 ; Octal

### Overflow
All numbers and registers are unsigned. If an operand is assigned an out-of-range constant at assembly-time, there will be an error. If a register goes out of range during run time, there will be an integer overflow (or underflow) and no error will be produced.
LD V0, 0x101 ; Error during assembly / LD V1, 0xFF / ADD V1, 2 ; Due to overflow, V1 = 1

### Math
The assembler is capable of resolving basic mathematical equations during assembly-time, so long as all operands are constants. The result is always truncated down to an integer. Operators have the same precedence as in C. Overflow / underflow will still raise an assembly-time error.
DEFINE x 10 / LD V0, x - 5 ; Sets V0 to 5 / LD V1, (x * 2) + (0x12 / 0b10) ; Sets V1 to 28 / LD V2, 3 ** 2 ; Sets V2 to 9 / LD V3, V1 + 2 ; Error, V3 not a constant / LD V4, 0xFF + 2 ; Error, 0x101 out of range

## Labels
A label is a case-insensitive bookmark for a memory address. All labels must be unique, and may not shadow any keywords or register names. Its value is computed during assembly, and resolves to the location in memory the next instruction is located. Most Chip-8 emulators begin program data at memory location 0x200. For the following example, remember that each instruction is 2 bytes long.
label1: ; label1 = 0x200 / label2: ; label2 = 0x200 / LD V0, 5 / label3: ; label3 = 0x202 / JP label1 ; Jump to 0x200

## The DEFINE Macro
The DEFINE macro is a label with an explicit value associated with it. All define macros should be placed at the top of the file, before any instructions are executed. While defines may be placed anywhere in the code, they will still affect any instructions that came before them. Notice that there is no comma between the macro’s key and value.
DEFINE x V0 / DEFINE value 5 / DEFINE JUMP jp / start: / LD x, value ; Sets V0 to 5 / LD y, value ; Sets V1 to 5, even though y is defined later / JUMP start ; Labels can even replace instructions / DEFINE y V1 / DEFINE 0xF 15 ; Error – Not in format /[A-Z_][0-9A-Z_]*/ / DEFINE I 6 ; Error – ‘I’ is a restricted keyword

DEFINE macros are even allowed to contain other symbols.

DEFINE x 10 / DEFINE y x * x / ADD V0, y ; Evaluates to 100

### Label Recursion Limit Exception
To prevent circular or never-ending DEFINE replacements, there is a hard limit (255) on how deeply nested the macro is. This limit is almost guaranteed to only be reached through unintentional circular references. Note that this limit does not apply to the number of simultaneous replacements, but rather the consecutive replacements that occur when the value of a DEFINE macro is the key of another.

; Standard circular reference will loop infinitely until the limit / ; is reached and an exception is thrown / DEFINE x y / DEFINE y x / ; While this will result in hundreds of replacements, it only has / ; a recursion level of 5 and therefore will not throw an exception / DEFINE a1 1 / DEFINE a2 a1 + a1 + a1 + a1 + a1 / DEFINE a3 a2 + a2 + a2 + a2 + a2 / DEFINE a4 a3 + a3 + a3 + a3 + a3 / DEFINE a5 a4 + a4 + a4 + a4 + a4 / DEFINE a6 a5 + a5 + a5 + a5 + a5

## Comments
Comments are immediately discarded during the preprocessing phase of the assembler, and have no effect on the program. However, they are integral to making Chip-8 code readable. For this assembler, comments begin with a semicolon (;) and may be placed anywhere on a line. Other assemblers may use double slash (//) or a pound sign (#) to denote a comment. Every source file should start with a comment block following this format:

; FILE: Adder.asm / ; AUTHOR: Michael Bianconi / ; CREATED: 12 December 2020 / ; DESCRIPTION: Performs simple addition based on user input

When commenting subroutines, it may be prudent to place a comment after every instruction. These comments should be structured such that reading only the comments will provide a good overview of what is happening. The following snippet is the main loop of a program that displays all 16 fonts.

loop: / SNE spriteIndex, numSprites ; If no more sprites, / JP end ; Jump to end / DRW x, y, spriteHeight ; Else, draw the current sprite / ADD spriteIndex, 1 ; Set spriteIndex to next sprite / LD F, spriteIndex ; Move I to next sprite / ADD x, spriteWidth ; Go to next column / SE x, displayWidth ; If not end of line, / JP loop ; Go draw the next sprite / LD x, 0 ; Else, set x back to 0 / ADD y, spriteHeight ; Move y down to the next line / ADD y, 1 ; Add 1 pixel of padding / JP loop ; Go draw the next sprite

## Indentation, Spacing, and Newlines
Each label and define should be placed un-indented on its own line. Instructions should be indented 8 spaces. The first operand should be indented another 8 spaces. Operands will be spaced one space apart. Comments should be aligned with each other within their subroutine.
DEFINE current V0 ; Holds the current sprite index / DEFINE x V1 ; Where to display sprite (x-axis) / DEFINE y V2 ; Where to display sprite (y-axis) / DEFINE _ VE ; Unused register / start: / LD F, current ; set I to the location of the current sprite / CLS ; clear previous sprite from screen / DRW x, y, 5 ; draw new sprite / ADD current, 1 ; advance to next sprite / SNE current, 0xF ; if looped through all sprites / JP end ; jump to end / LD _, K ; else wait for key press / JP start ; key was pressed, go to start / end: / SYS 0 ; Done

## Warnings
Instructions are 2 bytes long, and always start on an even-numbered memory address. The process of reading the next instruction is:

OP = (MEM[PC] << 8) | MEM[PC+1]

This has a very important implication: the program counter should always be an even number. However, there is no restriction from jumping the program counter to an odd-numbered address. When this happens, the lower 8 bits of the current instruction, and the upper 8 bits of the next instruction, will bitwise-OR’d together to create an entirely new instruction.

# Additional References
The Chip-8 Wikipedia page
Cowgod's Chip-8 Technical Reference